## Slide 1: Using Kokkos for Performant Cross-Platform Acceleration of Liquid Rocket Simulations
May 8, 2017
Dr. Michael Carilli
Contractor, ERC Incorporated
RQRC
AFRL-West

## Slide 2: PART 1: Integrating Kokkos with CASTLES What do you do when someone hands you 100,000 lines of Fortran and says “make this run on anything?”
PART 2: GPU-specific kernel optimizations
How do I make per-grid-point nested loops blazing fast?
Highly general/easily transferrable to other applications.

## Slide 3: CASTLES: Cartesian Adaptive Solver Technology for Large Eddy Simulations
CASTLES simulation of rotating detonation engine
(courtesy of Dr. Christopher Lietz)
A high-order Navier-Stokes solver for turbulent combustion
Written in Fortran
MPI parallelism, but no intra-process parallelism

## Slide 4
Control API
Timestepping
Time derivatives for physical quantities
Geometry
Handles spatial discretization
System
Specifies system of equations
Equations
Physics-independent quantities
Physics
Turbulence models
Detailed chemical kinetics
Chung Viscosity Model (ported to Kokkos)
Peng-Robinson Equation of State (ported to Kokkos)
Structure of CASTLES

## Slide 5: What is Kokkos?
C++ Framework. Claims “Performant cross platform parallelism”: write once, compile for many architectures.
Parallel patterns (for, reduce, scan) accept user-defined functors (like Thrust or Intel TBB)
Backends for Nvidia GPU, Intel Xeon, Xeon Phi, IBM Power8, others.
“View” data structures provide optimal layout:
cache-order access when compiled for CPU, coalesced access when compiled for GPU.
Thrust offers similar multi-platform backends – but less low level control and does not abstract data layout.
Programming Guide:
https://github.com/kokkos/kokkos/blob/master/doc/Kokkos_PG.pdf
At GTC 2017:
S7344 - Kokkos : The C++ Performance Portability Programming Model
S7253 - Kokkos Hierarchical Task-Data Parallelism for C++ HPC Applications

## Slide 6: Enabling Kokkos in CASTLES
CASTLES is a Cartesian solver written in Fortran 90.
Identify performance limiting subroutines
Port Fortran subroutines to Kokkos C++
Optimize ported routines
Minimally invasive integration of Kokkos C++ with CASTLES (“code surgery”)

## Slide 7: Identify critical subroutines – CPU profile
CPU profile for 5 chemical species
Quick and easy single-process profile with nvprof:
I like the top-down view.
Easy to see global structure and call chains.
Can also do bottom up profile (default)
nvprof --cpu-profiling on
--cpu-profiling-mode top-down ./CASTLES.x

## Slide 8: Identify critical subroutines – CPU profile
Quick and easy single-process profile with nvprof:
I like the top-down view.
Easy to see global structure and call chains.
Can also do bottom up profile (default)
Looks like those “preos” and “chung” routines
are burning a lot of time
CPU profile for 5 chemical species
======== CPU profiling result (top down):
51.29% clone
| 51.29% start_thread
| 51.29% orte_progress_thread_engine
| 51.29% opal_libevent2021_event_base_loop
| 51.29% poll_dispatch
| 51.29% poll
48.54% MAIN__
| 48.45% interfacetime_mp_maintimeexplicit_
| | 48.45% interfacetime_mp_rhstimessp34_
| | 29.77% interfacegeom_mp_rhsgeomrescalc_
| | | 15.46% interfacegeom_mp_rhsgeom3dresad1lr_
| | | | 15.35% interfacesysexternal_mp_rhssysupdiss_
| | | | | 15.35% interfacesysinternal_mp_rhssysscalarupdiss_
| | | | | 9.85% eosmodule_mp_eoscalcrhoh0fromtp_
| | | | | | 9.64% eosmodule_mp_eosrhohfromtpprop_
| | | | | | 9.64% preosmodule_mp_preosrhohfromtpprop_
...
| | | | | 5.18% eosmodule_mp_eosgammajacobianproperties_
| | | | | 5.10% preosmodule_mp_preosgammajacobianproperties_
...
| | | 13.90% interfacegeom_mp_rhsgeom3dviscres2_
| | | | 13.84% interfacesysexternal_mp_rhssysviscflux_
| | | | 13.32% preosmodule_mp_preosviscousfluxproperties_
| | | | | 7.85% chungtransmodule_mp_chungcalctransprop_
...
| | | | | 3.27% preosmodule_mp_preoscriticalstate_
...
| | 18.33% interfacegeom_mp_bcgeomrescalc_
| | | 14.77% interfacegeom_mp_bcgeomsubin_
| | | | 14.77% interfaceeqnfluids_mp_bcfluidseqnsubin_velocity_
| | | | 14.77% preosmodule_mp_preoscalctfromhp_
...
| | | 3.56% interfacesysexternal_mp_stepsys3dcalcqadd_
| | | 3.53% eosmodule_mp_eosthermalproperties_
| | | | 3.50% preosmodule_mp_preosthermalproperties_
...
nvprof --cpu-profiling on
--cpu-profiling-mode top-down ./CASTLES.x

## Slide 9: Peng-Robinson equation of state and Chung transport model
Peng-Robinson Equation of State:
Computes physical properties (density, enthalpy, etc.) for real gas mixtures at high pressure
Chung Transport Model:
Computes transport properties (viscosity, thermal conductivity, mass diffusivity) for real gas mixtures at high pressure
Many underlying subroutines shared between Chung and P-R.
Properties are computed individually per cell
(or interpolated points at cell interfaces),
so trivially parallel
Relatively small data transfer, lengthy computation
=> perfect for GPU offload
Input/output data scales linearly with number of species (NS)
Subroutines contain single loops, double loops, triple loops over NS
=> runtime scales like a*NS + b*NS2 + c*NS3
Occupies majority of CASTLES runtime for ns >= 4ish
Chart: Cubic polynomial fits P-R scaling with number of chemical species
| 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
Runtime on GPU | 4.6586e-08 | 7.3785e-08 | 1.0525e-07 | 1.4323e-07 | 1.8772e-07 | 2.5933e-07 | 3.2444e-07 | 4.0148e-07 | 4.8828e-07 | 6.2391e-07 | 7.364e-07 | 8.6589e-07 | 1.0059e-06 | 1.2261e-06 | 1.3997e-06 | 1.5914e-06 | 1.794e-06 | 2.1159e-06 | 2.3655e-06 | 2.6367e-06 | 2.9188e-06 | 3.3637e-06 | 3.6784e-06 | 4.0365e-06 | 4.4162e-06 | 5.0022e-06 | 5.4145e-06 | 5.8919e-06 | 6.3585e-06 | 7.0964e-06 | 7.6063e-06 | 8.1706e-06 | 8.7674e-06 | 9.6788e-06 | 1.0326e-05 | 1.1035e-05 | 1.1773e-05 | 1.2862e-05 | 1.3628e-05 | 1.4428e-05 | 1.5336e-05 | 1.6623e-05 | 1.7556e-05 | 1.8533e-05 | 1.9661e-05 | 2.1238e-05
Column1

## Slide 10: Architecture of my Kokkos framework
Frame
// Owns and allocates TVProperties object
TVProperties* tvproperties;
// Controls Kokkos initialization/finalization
void initialize(…);
void finalize(…);
TVProperties* gettvproperties();
Designed for minimally-invasive operation alongside large Fortran code.
Everything is controlled from Fortran through a single lightweight global Frame object.
Kernel launches and data comms are referred to TVProperties* owned by Frame.

## Slide 11: Architecture of my Kokkos framework
Frame
// Owns and allocates TVProperties object
TVProperties* tvproperties;
// Controls Kokkos initialization/finalization
void initialize(…);
void finalize(…);
TVProperties* gettvproperties();
Designed for minimally-invasive operation alongside large Fortran code.
TVProperties
// Owns and allocates TVImpl object
TVImpl* impl;
// Public member functions to communicate data
// to/from Views in TVImpl
void populateInputStripe(…);
void populateOutputStripe(…);
void populateprEOSSharedData(…);
void populatechungSharedData(…);
…
// Public member functions to launch collections of
// kernels
void prEOSThermalProperties(…);
void prEOSViscousProperties(…);
void eosGammaJacobianProperties(…);
…
Everything is controlled from Fortran through a single lightweight global Frame object.
Kernel launches and data comms are referred to TVProperties* owned by Frame.

## Slide 12: Architecture of my Kokkos framework
Frame
// Owns and allocates TVProperties object
TVProperties* tvproperties;
// Controls Kokkos initialization/finalization
void initialize(…);
void finalize(…);
TVProperties* gettvproperties();
Designed for minimally-invasive operation alongside large Fortran code.
TVProperties
// Owns and allocates TVImpl object
TVImpl* impl;
// Public member functions to communicate data
// to/from Views in TVImpl
void populateInputStripe(…);
void populateOutputStripe(…);
void populateprEOSSharedData(…);
void populatechungSharedData(…);
…
// Public member functions to launch collections of
// kernels
void prEOSThermalProperties(…);
void prEOSViscousProperties(…);
void eosGammaJacobianProperties(…);
…
TVImpl
// Contains members of TVProperties that don’t need
// external visibility (pimpl idiom)
// Owns and allocates Kokkos Views
View1DType T;
View1DType P;
View1DType Yi;
…(several dozen of these)
// Owns std::unordered_maps to launch kernels
// and communicate data by name
unordered_map<string,View1DType>
select1DViewByName;
unordered_map<string,View2DType>
select2DViewByName;
// Owns Launcher for each kernel
// (lightweight wrapper with string identifier,
// inherits common timing routines from
// LauncherBase)
unordered_map<string,LauncherBase*> launchers;
void safeLaunch(…);
Everything is controlled from Fortran through a single lightweight global Frame object.
Kernel launches and data comms are referred to TVProperties* owned by Frame.

## Slide 13: For modularity and consistency: one subroutine->one kernel
There are roughly 50 of these that serve as building blocks.
Fortran subroutine:
Operates on a single grid point at a time
Kokkos kernel launch:
Operates on nActivePoints grid points in parallel
Kokkos Views,
captured by value from members of TVImpl)
(View copy constructor is a lightweight shallow copy)
parallel_for( tvimpl->nActivePoints,
KOKKOS_LAMBDA( const int& t )
{
c(t) = sqrt( rho(t)*hT(t)/
( rho(t)*rhoP(t)*hT(t)
+ rhoT(t)*( 1.0-rho(t)*hP(t) ) ) )
} );
pure subroutine prEOSCalcSoundSpeed&
( rho, rhop, rhoT, hp, hT, c )
use useGENKindDefs, only: dp
implicit none
real(dp), intent(in) :: rho, rhop, rhoT, hp, hT
real(dp), intent(out) :: c
c = sqrt( rho*ht/&
( rho*rhop*ht + rhot*( 1.0_dp-rho*hp ) ) )
end subroutine prEOSCalcSoundSpeed
Parallel pattern
User-defined functor (lambda)
Parallel work index t

## Slide 14
Chart: GPU* vs. Serial Fortran**
| Fortran (Serial)
5 species | 32.6
10 | 24.57
20 | 18.74
50 | 15.5
GPU Speedups for Standalone Peng-Robinson
* Nvidia Kepler K40
** Intel Xeon E5-2620 v3 CPU
Good speedups overall.
GPU speedup is better for fewer species (NS)
Smaller per-thread data set => improved cache hit rates on GPU
Smaller inner loops => vectorization less efficient on CPU
(a combination of GPU doing better and CPU doing a bit worse)

## Slide 15: Integrating Kokkos with CASTLES: Interface Functions
C++ Interface functions (callable from Fortran) tell Frame object to initialize/finalize Kokkos, launch collections of kernels, or communicate data.
extern “C” void frame_initialize_( int device_id,
int nGridPoints
int ns
int nq
int iTurb )
{
frame.initialize( device_id, // GPU device to select
nGridPoints, // Chunk size for Kokkos launches
ns, // Num chemical species
nq, // Utility values
iTurb );
}
extern “C” void frame_tvproperties_eosthermalandviscousproperties_(
int nActivePoints )
{
frame.gettvproperties()->eosThermalAndViscousProperties(
nActivePoints );
}
call frame_tvproperties_eosthermalandviscousproperties&
( %VAL( NumThisStripe ) )
Interface function to initialize Kokkos and allocate storage
Interface function to launch collection of kernels for thermal and viscous properties
Corresponding Fortran call
! Compute KokkosDeviceID as MPI rank%num devices
! Num devices is supplied by input file
call frame_initialize( %VAL( KokkosDeviceID,&
%VAL( KokkosMaxBlock ),&
%VAL( nspe ),&
%VAL( nq ),&
%VAL( iTurbType ) )
Corresponding Fortran call

## Slide 16: Integrating Kokkos with CASTLES: Interface Functions
C++ Interface functions (callable from Fortran) tell Frame object to initialize/finalize Kokkos, launch collections of kernels, or communicate data.
extern “C” void frame_initialize_( int device_id,
int nGridPoints
int ns
int nq
int iTurb )
{
frame.initialize( device_id, // GPU device to select
nGridPoints, // Chunk size for Kokkos launches
ns, // Num chemical species
nq, // Utility values
iTurb );
}
extern “C” void frame_tvproperties_eosthermalandviscousproperties_(
int nActivePoints )
{
frame.gettvproperties()->eosThermalAndViscousProperties(
nActivePoints );
}
call frame_tvproperties_eosthermalandviscousproperties&
( %VAL( NumThisStripe ) )
Interface function to initialize Kokkos and allocate storage
Interface function to launch collection of kernels for thermal and viscous properties
Corresponding Fortran call
! Compute KokkosDeviceID as MPI rank%num devices
! Num devices is supplied by input file
call frame_initialize( %VAL( KokkosDeviceID,&
%VAL( KokkosMaxBlock ),&
%VAL( nspe ),&
%VAL( nq ),&
%VAL( iTurbType ) )
Corresponding Fortran call
Disallow name mangling by C++ compiler
Trailing _ expected by Fortran linker
Pass integers by value

## Slide 17: Communicating Data
Data communication must translate between 4D Fortran pointers (x,y,z,dataindx) and Kokkos Views. For some computations, a halo of fringe points must be ignored.
Fortran <-> C++ communication works as follows:
C++ framework receives double* from Fortran
Iterates linearly through x,y,z values. Extracts volume of data to Views, skipping fringe points.
In Views, x,y,z indices are flattened into a single parallel-work index, t.
After computation, reverse the process, copying data from Views back into double* storage with data layout expected by Fortran.
C++ framework must know xdim, ydim, zdim, and fringe boundaries to unpack and repack data. No free lunch here. Annoying indexing.
! Name tag of destination View
tag = “Q”//char(0)
call frame_castles_populateinputstripe( tag,&
Q,& ! 4D Fortran pointer, source of copy
%VAL( NumX ), %VAL( NumY ), %VAL( NumZ ),&
%VAL( SptX ), %VAL( EptX ),&
%VAL( SptY ), %VAL( EptY ),&
%VAL( SptZ ), %VAL( EptZ ),&
%VAL( SptData ), %VAL( EptData ),&
%VAL( SptStripe ), %VAL(EptStripe ) )
extern “C” void frame_castles_populateinputstripe_(
const char name[8], // Name tag of destination View
double* data, // Source pointer (from Fortran)
int nx, int ny, int nz, // Dims of block (including fringes)
int SptX, int EptX, // Fringe boundaries in x-direction
int SptY, int EptY, // “ y-direction
int SptZ, int EptZ, // “ z-direction
int SptData, // Start of data region (slowest index)
int EptData, // End of data region
int stripeStart, // Start and end of selected x,y,z
int stripeEnd ) // stripe; used when looping over block
// in chunks (stripes) of fixed size
{
frame.gettvproperties()->populateInputStripe( name,
data, nx, ny, nz, SptX, EptX, SptY, EptY,
SptZ, EptZ, SptData, EptData, stripeStart, stripeEnd );
}
C++ interface function
Corresponding Fortran call

## Slide 18: Data marshalling challenges
Challenge #1:
Kokkos launches need enough parallel work (enough grid points) to saturate GPU.
Solution:
Ensure availability of this process’ entire block of data where Kokkos interface functions are called.
Restructuring some Fortran calling functions was required, but minimal impact to code overall.
Challenge #2:
Block size handled by each process may change between timesteps, due to adaptive mesh refinement. Prefer not to reallocate Kokkos data structures, or worse, exhaust GPU memory.
Solution:
Launch Kokkos computations via a loop over this process’ block in chunks of largeish but fixed size “KokkosMaxBlock.”
KokkosMaxBlock is a tuning parameter in input file, large enough that one chunk’s launch should saturate GPU when
10-20 processes are sharing the GPU via Nvidia Multi-Process Service.
KokkosMaxBlock = 8192 or 12288 usually gives good performance.

## Slide 19: Cluster-level concerns: Multiple GPUs per node
** Minor Caveat: If MPI process is bound to a specific set of cores, Kokkos does not try to select the optimally hardware co-located GPU (this may have changed since last I checked).
Standalone Kokkos application:
Within code:
To run:
Kokkos will detect available GPUs and assign MPI ranks to GPUs round robin.**
My application (embedded within a big Fortran code):
Pass num GPU devices per node in Fortran input file:
Within Fortran, compute device to use as (MPI rank%num devices):
…and call the interface function to initialize Kokkos:
Finally, within C++ frame.initialize():
No need for arguments to executable.
Kokkos::initialize( int& argc, char* argv[] );
$ mpirun -n numprocs ./myKokkosApp \
> --kokkos-ndevices=2
&KokkosInputs
KokkosNumDevices = 2
...
/
call MPI_COMM_RANK( MPI_COMM_WORLD, rank, ierror )
KokkosDeviceID = mod( rank, KokkosNumDevices )
Kokkos::InitArguments args;
args.device_id = KokkosDeviceID;
Kokkos::initialize( args );
call frame_initialize( %VAL( KokkosDeviceID ), ... )

## Slide 20: Cluster-level concerns: Nvidia Multi-Process Service (MPS)
Without MPS:
Each MPI process has its own CUDA context.
Multi-process profile shows one process at a time using a given GPU.
With MPS:
Multiple processes can share a given GPU simultaneously.
Better utilization and dramatic speedup for my application, and easy to use
(just run nvidia-cuda-mps-control –d on each compute node to start the daemons).
See http://on-demand.gputechconf.com/gtc/2016/presentation/s6142-jiri-kraus-multi-gpu-programming-mpi.pdf
Kernels from different processes do not overlap
Kernels from different processes overlap
For small NS, turning on MPS makes overall application up to 3X faster

## Slide 21
GPU Speedup of Overall CASTLES+Kokkos
Production-style runs:
40 MPI ranks on 2 nodes.
CASTLES Fortran uses 20 CPUs/node only.
CASTLES+Kokkos uses 20 CPUs + 2 GPUs/node.
Speedup computed as (CASTLES Fortran runtime)/(Castles+Kokkos runtime)
2.5-3.0X consistently observed across range of desirable problem parameters.
Chart: Speedup with Kokkos
| 5 species | 20 species | 40 species
1st order | 2.4972 | 2.585 | 2.7705
9th order | 2.7346 | 2.7879 | 2.8259

## Slide 22
Kokkos on CPU matches Fortran on CPU
Often, naively porting Fortran to C++ results in a slowdown (e.g. compiler has a harder time optimizing/vectorizing loops).
Need to use hardware-specific (Intel) compiler and manually tweak vector pragmas for some in-kernel loops, but in the end
Kokkos C++ is as fast as original Fortran.
Can the Kokkos-enabled codebase compile for CPU as well as GPU, with good performance?
KOKKOS_LAMBDA( const int& t )
{
#ifdef KOKKOS_HAVE_CUDA
…GPU-optimal code goes here…
#else
…CPU-optimal code goes here…
#endif
}
To compile for CPU, just change arguments to makefile (see Kokkos documentation).
nvcc ignores Intel pragmas. Kokkos-enabled source code is (almost entirely) same as used for GPU.
Only two kernels needed moderately divergent code for good performance on both CPU and GPU.
Kokkos build system provides pragmas to select different code when compiling for different hardware.
Kokkos promise of “performant cross-platform parallelism” more or less fulfilled.
Chart: Test case: NS=5, 163 grid points, 50 timesteps
| CASTLES+Fortran (1 CPU) | CASTLES+Kokkos OpenMP (1 thread)**
1st order | 30.2 | 28.5
**KMP_AFFINITY=compact,1,granularity=core

## Slide 23
Node level performance + comparison with Xeon Phi
Kokkos runs on Xeon Phis in native mode.
MPI+Kokkos processes see Phi cores as additional CPU cores.
Kokkos computations are not offloaded GPU-style.
Entire process runs on a set of Phi cores just like on a multicore CPU.
GPUs are offload coprocessors, so can’t compare Phi vs. GPU apples-to-apples. But we can get an idea at node level.
Chart: Runtime for fixed problem size 1203, NS=5, 1st order, 20 timesteps
| CASTLES Fortran: 20 CPU cores | CASTLES+Kokkos: 20 CPU cores + 2 GPUs | CASTLES+Kokkos: Xeon Phi Knight's Corner | CASTLES+Kokkos: Xeon Phi Knight's Landing
Runtime | 200 | 68 | 726 | 151

## Slide 24
System details
2x10 core Intel Xeon E5-2650 v3
Config file for Intel MPI:
-genv I_MPI_PIN_DOMAIN=auto:compact
-n 20 ./CASTLES.kokkos
Although cores are hyperthreaded (40 logical cores available),
adding more processes does not improve performance significantly.
2x10 core Intel Xeon E5-2650 v3
+ 2 Kepler K40 GPUs.
KokkosMaxBlock = 12288
Same MPI config as CASTLES Fortran.
One Knight’s Corner 5110P (60 cores, 240 logical processors).
KokkosMaxBlock = 1024
Config file for Intel MPI:
-genv I_MPI_PIN_DOMAIN=4:compact –genv OMP_NUM_THREADS 4
-host mic0 –n 60 –env KMP_AFFINITY=compact,granularity=core ./CASTLES.knc
One Knight’s Landing 7230 (64 cores, 256 logical processors), flat memory mode, SNC-4 cluster mode
KokkosMaxBlock = 1024
Config file for Intel MPI:
-genv I_MPI_PIN_DOMAIN=1:compact -genv OMP_NUM_THREADS 1
-n 256 –env KMP_AFFINITY=compact,granularity=core numactl –m 4,5,6,7 ./CASTLES.knl
Numactl –m 4,5,6,7 enforces first-touch allocation in onboard high-bandwidth memory.
I experimented with fewer MPI processes, bigger domains, and more OpenMP threads,
and found 256 procs with 1 thread/proc best.
Chart: Runtime for fixed problem size 1203, NS=5, 1st order, 20 timesteps
| CASTLES Fortran: 20 CPU cores | CASTLES+Kokkos: 20 CPU cores + 2 GPUs | CASTLES+Kokkos: Xeon Phi Knight's Corner | CASTLES+Kokkos: Xeon Phi Knight's Landing
Runtime | 200 | 68 | 726 | 151

## Slide 25: PART 1: Integrating Kokkos with CASTLES What do you do when someone hands you 100,000 lines of Fortran and says “make this run on anything?”
PART 2: GPU-specific kernel optimizations
How do I make per-grid-point nested loops blazing fast?
Highly general/easily transferrable to other applications.

## Slide 26
“Embarrassingly parallel,” and inner loops are simple…
but achieving high performance is an interesting problem!
// Loop over N grid points (trivially parallel)
for( int t = 0; t < N; t++ )
for( int y = 0; y < NS; y++ ) // NS ~ up to 50ish
for( int x = 0; x < NS; x++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t] + bx[x*N+t]*by[y*N+t];
P-R and Chung involve nested inner loops over chemical species NS (can be 50 or more).
Independent calculations for each grid point.
Toy example (shown as serial loop over grid points):
Bandwidth-Bound Per-Grid-Point Inner Loops
Arrays of size NS*N that store
per-grid-point input data

## Slide 27
“Embarrassingly parallel,” and inner loops are simple…
but achieving high performance is an interesting problem!
// Loop over N grid points (trivially parallel)
for( int t = 0; t < N; t++ )
for( int y = 0; y < NS; y++ ) // NS ~ up to 50ish
for( int x = 0; x < NS; x++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t] + bx[x*N+t]*by[y*N+t];
P-R and Chung involve nested inner loops over chemical species NS (can be 50 or more).
Independent calculations for each grid point.
Toy example (shown as serial loop over grid points):
Several X-dependent loads
Several Y-dependent loads
Bandwidth-Bound Per-Grid-Point Inner Loops

## Slide 28: Testing Parameters
Tesla K40 GPU
  12 GB device memory
  15 Kepler SMs
Kepler architecture:
  192 single-precision cores and 64 double-precision cores per SM
  100% occupancy = 2048 active threads per SM
  65,536 registers available per SM
  64KB L1 cache/shared memory per SM, configurable as either 48 KB L1 + 16 KB shared, 32 KB L1 + 32 KB shared, or 16 KB L1 + 32 KB shared
  48 KB read-only cache (declare pointers with const __restrict__ to use this**)
Compiled with nvcc version 7.5, opt-in L1 caching, verbose to see register/local mem use, targeting compute capability 3.5
nvcc -Xptxas=“-dlcm=ca” –Xptxas=“-v” –arch=sm_35 kernels.cu
Runtime call to cudaDeviceSetCacheConfig(cudaFuncCachePreferL1) to set the 48 KB L1 + 16 KB shared option in case the compiler chooses to load via L1
For timing purposes, I use N=2048*120, NS=64, 960 blocks, 256 threads/block. On a K40 with 15 SMs, this is 8 full waves.
Kernel wall times averaged over 100 trials.
** In subsequent examples, I do not write “const.” Although the Kepler Tuning Guide is pretty adamant that writing “const” is necessary to trigger loads via the 48 KB read-only cache, I found that for toy kernels presented here, the compiler uses read-only cache even if “const” is omitted.

## Slide 29
__global__ void naive( double* __restrict__ ax, double* __restrict__ bx,
double* __restrict__ ay, double* __restrict__ by, double* __restrict__ output )
{
// Ordinarily we might wrap this in a grid stride loop…omitted to save space.
int t = threadIdx.x + blockIdx.x*blockDim.x;
#pragma unroll 1 // Disallow compiler unrolling so we know what’s happening.**
for( int y = 0; y < NS; y++ )
#pragma unroll 1
for( int x = 0; x < NS; x++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t] + bx[x*N+t]*by[y*N+t];
}
** If we omit the “#pragma unroll 1”s and let the compiler unroll as it wishes, register use goes up (as expected), occupancy falls, and the “naïve” kernel’s performance worsens. 100% occupancy is not always essential, but in this case, explicitly including the pragmas is better than relying on compiler heuristics.
Naïve Cuda Kernel – one thread per grid point

## Slide 30
__global__ void naive( double* __restrict__ ax, double* __restrict__ bx,
double* __restrict__ ay, double* __restrict__ by, double* __restrict__ output )
{
// Ordinarily we might wrap this in a grid stride loop…omitted to save space.
int t = threadIdx.x + blockIdx.x*blockDim.x;
#pragma unroll 1 // Disallow compiler unrolling so we know what’s happening.
for( int y = 0; y < NS; y++ )
#pragma unroll 1
for( int x = 0; x < NS; x++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t] + bx[x*N+t]*by[y*N+t];
}
Grid point index “t” is fast index for coalescing
Naïve Cuda Kernel – one thread per grid point

## Slide 31
__global__ void naive( double* __restrict__ ax, double* __restrict__ bx,
double* __restrict__ ay, double* __restrict__ by, double* __restrict__ output )
{
// Ordinarily we might wrap this in a grid stride loop…omitted to save space.
int t = threadIdx.x + blockIdx.x*blockDim.x;
#pragma unroll 1 // Disallow compiler unrolling so we know what’s happening.
for( int y = 0; y < NS; y++ )
#pragma unroll 1
for( int x = 0; x < NS; x++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t] + bx[x*N+t]*by[y*N+t];
}
Grid point index “t” is fast index for coalescing
y-dependent loads should hit in cache (or be promoted to registers) during loop over x.
I find that manually hoisting y-loads to a register does not affect performance.
Naïve Cuda Kernel – one thread per grid point

## Slide 32
__global__ void naive( double* __restrict__ ax, double* __restrict__ bx,
double* __restrict__ ay, double* __restrict__ by, double* __restrict__ output )
{
// Ordinarily we might wrap this in a grid stride loop…omitted to save space.
int t = threadIdx.x + blockIdx.x*blockDim.x;
#pragma unroll 1 // Disallow compiler unrolling so we know what’s happening.
for( int y = 0; y < NS; y++ )
#pragma unroll 1
for( int x = 0; x < NS; x++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t] + bx[x*N+t]*by[y*N+t];
}
Grid point index “t” is fast index for coalescing
y-dependent loads should hit in cache (or be promoted to registers) during loop over x.
I find that manually hoisting y-loads to a register does not affect performance.
Each x-load is used only once per outer y-loop iteration.
Probably won’t hit in cache on the next outer y-loop iteration.
Naïve Cuda Kernel – one thread per grid point

## Slide 33
Kernel “naïve” is strongly bandwidth-bound, and accesses are already coalesced. What should we do?
__global__ void naive( double* __restrict__ ax, double* __restrict__ bx,
double* __restrict__ ay, double* __restrict__ by, double* __restrict__ output )
{
// Ordinarily we might wrap this in a grid stride loop…omitted to save space.
int t = threadIdx.x + blockIdx.x*blockDim.x;
#pragma unroll 1 // Disallow compiler unrolling so we know what’s happening.
for( int y = 0; y < NS; y++ )
#pragma unroll 1
for( int x = 0; x < NS; x++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t] + bx[x*N+t]*by[y*N+t];
}
Grid point index “t” is fast index for coalescing
Naïve Cuda Kernel – one thread per grid point
Chart: Runtime
| Naïve
Runtime | 0.138
y-dependent loads should hit in cache (or be promoted to registers) during loop over x.
I find that manually hoisting y-loads to a register does not affect performance.
Each x-load is used only once per outer y-loop iteration.
Probably won’t hit in cache on the next outer y-loop iteration.

## Slide 34: Standard CPU-informed strategy: tile the loop?
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t] + bx[x*N+t]*by[y*N+t];
Recall why loop tiling helps on CPU:

## Slide 35: Standard CPU-informed strategy: tile the loop?
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t] + bx[x*N+t]*by[y*N+t];
X-dependent loads should hit in cache for the inner y-loop, and be reused TILE_FACTOR times
Recall why loop tiling helps on CPU:

## Slide 36: Standard CPU-informed strategy: tile the loop?
(in fact, for a typical CPU cache and modest values of NS like 64, the entire working set should easily fit in cache, and it’s not necessary to tile the loop at all.)
Pretty standard stuff…but do we expect this to work on a Kepler GPU?
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t] + bx[x*N+t]*by[y*N+t];
X-dependent loads should hit in cache for the inner y-loop, and be reused TILE_FACTOR times
Each x-iteration now treats TILE_FACTOR y-iterations instead of just one.
TILE_FACTOR y-dependent loads should hit in cache on each iteration of x-loop
Recall why loop tiling helps on CPU:

## Slide 37: Loop tiling on GPU
__global__ void tiled(…same args as naïve…)
{
int t = threadIdx.x + blockIdx.x*blockDim.x;
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t]
+ bx[x*N+t]*by[y*N+t];
}

## Slide 38: Loop tiling on GPU
Tiling is worse than naïve. Cache per grid point (thread) is just too small.
Read-only cache and L1 cache are only 48 KB each.
Whichever compiler chooses to use:
100% occupancy = 2048 threads
48 KB/2048 threads = only 3 doubles’ worth of cache per thread.
__global__ void tiled(…same args as naïve…)
{
int t = threadIdx.x + blockIdx.x*blockDim.x;
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t]
+ bx[x*N+t]*by[y*N+t];
}
Chart: Tiled Loop Runtimes
| Naïve | TILE_FACTOR 2 | 4 | 8
Runtime | 0.138 | 0.217 | 0.207 | 0.196

## Slide 39: Loop tiling on GPU
Tiling is worse than naïve. Cache per grid point (thread) is just too small.
Read-only cache and L1 cache are only 48 KB each.
Whichever compiler chooses to use:
100% occupancy = 2048 threads
48 KB/2048 threads = only 3 doubles’ worth of cache per thread.
nvprof confirms poor hit rates (results for TILE_FACTOR 2 shown):**
nvprof --kernels ::tiled:1 –metrics \
nc_cache_global_hit_rate,tex_cache_hit_rate ./a.out
. . . Min Max
. . . Non-Coherent Global Hit Rate 0.85% 0.85%
. . . Texture Cache Hit Rate 0.65% 0.65%
__global__ void tiled(…same args as naïve…)
{
int t = threadIdx.x + blockIdx.x*blockDim.x;
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t]
+ bx[x*N+t]*by[y*N+t];
}
** As mentioned previously, the compiler appears to use read-only/texture cache for loads.
I’m not sure why there are separate metrics to describe “read-only cache accesses” and “texture cache accesses” (it’s the same hardware). Perhaps some Cuda ninja can explain?
Chart: Tiled Loop Runtimes
| Naïve | TILE_FACTOR 2 | 4 | 8
Runtime | 0.138 | 0.217 | 0.207 | 0.196

## Slide 40: Tile with reduced occupancy
100% occupancy is not a strict requirement for peak performance.
Lower occupancy = more cache per grid point.**
__global__ void tiled_reduced_occupancy(…)
{
extern __shared__ int smem[];
int t = threadIdx.x + blockIdx.x*blockDim.x;
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t]
+ bx[x*N+t]*by[y*N+t];
}
** See “GPU Memory Bootcamp II: Beyond Best Practices” from GTC 2015 ( http://on-demand.gputechconf.com/gtc/2015/presentation/S5376-Tony-Scudiero.pdf )
for a more detailed discussion of occupancy vs. hit rate.

## Slide 41: Tile with reduced occupancy
100% occupancy is not a strict requirement for peak performance.
Lower occupancy = more cache per grid point.**
Manually suppress occupancy by giving each block “dummy” shared memory.
For example: 16 KB shared memory is available on each SM.
If we assign each block 4096 B smem, only 4 blocks can fit on each SM.
4*256 = 1024 threads. 1024/2048 = 50% occupancy.
__global__ void tiled_reduced_occupancy(…)
{
extern __shared__ int smem[];
int t = threadIdx.x + blockIdx.x*blockDim.x;
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t]
+ bx[x*N+t]*by[y*N+t];
}
** See “GPU Memory Bootcamp II: Beyond Best Practices” from GTC 2015 ( http://on-demand.gputechconf.com/gtc/2015/presentation/S5376-Tony-Scudiero.pdf )
for a more detailed discussion of occupancy vs. hit rate.

## Slide 42: Tile with reduced occupancy
Mostly worse than naïve.
Chart: Runtime vs. Occupancy
| Naïve | TILE_FACTOR 2 | TILE_FACTOR 4 | TILE_FACTOR 8
50% (4 KB smem/block) | 0.189 | 0.219 | 0.195
25% (8 KB smem/block) | 0.138 | 0.255 | 0.26 | 0.253
12.5% (16 KB smem/block) | 0.173 | 0.127 | 0.21
100% occupancy is not a strict requirement for peak performance.
Lower occupancy = more cache per grid point.
Manually suppress occupancy by giving each block “dummy” shared memory.
For example: 16 KB shared memory is available on each SM.
If we assign each block 4096 B smem, only 4 blocks can fit on each SM.
4*256 = 1024 threads. 1024/2048 = 50% occupancy.
__global__ void tiled_reduced_occupancy(…)
{
extern __shared__ int smem[];
int t = threadIdx.x + blockIdx.x*blockDim.x;
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t]
+ bx[x*N+t]*by[y*N+t];
}

## Slide 43: Tile with reduced occupancy
Chart: Runtime vs. Occupancy
| Naïve | TILE_FACTOR 2 | TILE_FACTOR 4 | TILE_FACTOR 8
50% (4 KB smem/block) | 0.189 | 0.219 | 0.195
25% (8 KB smem/block) | 0.138 | 0.255 | 0.26 | 0.253
12.5% (16 KB smem/block) | 0.173 | 0.127 | 0.21
Mostly worse than naïve. Sweet spot at TILE_FACTOR 4, 12.5% occupancy can be explained by cache hits:
nvprof --kernels ::tiled_reduced_occupancy:4 --metrics achieved_occupancy,nc_cache_global_hit_rate,tex_cache_hit_rate ./a.out
. . . Achieved Occupancy 0.124771 0.124771
. . . Non-Coherent Global Hit Rate 75.81% 75.81%
100% occupancy is not a strict requirement for peak performance.
Lower occupancy = more cache per grid point.
Manually suppress occupancy by giving each block “dummy” shared memory.
For example: 16 KB shared memory is available on each SM.
If we assign each block 4096 B smem, only 4 blocks can fit on each SM.
4*256 = 1024 threads. 1024/2048 = 50% occupancy.
__global__ void tiled_reduced_occupancy(…)
{
extern __shared__ int smem[];
int t = threadIdx.x + blockIdx.x*blockDim.x;
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay[y*N+t]
+ bx[x*N+t]*by[y*N+t];
}

## Slide 44: Tile using both L1 and read-only cache
** On Kepler, local loads are cached in L1. On Maxwell, L1/tex is a single unified cache, and local loads are cached in L2 only. Therefore, I expect tiling with
local memory to be helpful on Kepler only. Maxwell has separate hardware for shared memory, so you could try using thread-local smem arrays instead.
See https://devblogs.nvidia.com/parallelforall/fast-dynamic-indexing-private-arrays-cuda/ for an in-depth discussion of where the compiler places thread-local arrays.
See http://docs.nvidia.com/cuda/kepler-tuning-guide/#l1-cache and http://docs.nvidia.com/cuda/maxwell-tuning-guide/#l1-cache for microarchitecture details.
__global__ void tiled_local_arrays(…)
{
double ay_local[TILE_FACTOR]; // Thread-local arrays
double by_local[TILE_FACTOR]; // (placed in local memory)
int t = threadIdx.x + blockIdx.x*blockDim.x;
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
{
for( int y = yy; y < yy + TILE_FACTOR; y++ )
{
ay_local[y-yy] = ay[y*N+t];
by_local[y-yy] = by[y*N+t];
}
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay_local[y-yy]
+ bx[x*N+t]*by_local[y-yy];
}
}
On Kepler, 48 KB read-only cache and 64 KB L1+shared cache are independent. Use both!
Tile using thread-local arrays :
(placed in a local memory stack frame. Allocated in device global memory, but cached in L1)**

## Slide 45: Tile using both L1 and read-only cache
__global__ void tiled_local_arrays(…)
{
double ay_local[TILE_FACTOR]; // Thread-local arrays
double by_local[TILE_FACTOR]; // (placed in local memory)
int t = threadIdx.x + blockIdx.x*blockDim.x;
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
{
for( int y = yy; y < yy + TILE_FACTOR; y++ )
{
ay_local[y-yy] = ay[y*N+t];
by_local[y-yy] = by[y*N+t];
}
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay_local[y-yy]
+ bx[x*N+t]*by_local[y-yy];
}
}
Thread-local arrays for
Y-dependent loads (cached in L1)
On Kepler, 48 KB read-only cache and 64 KB L1+shared cache are independent. Use both!
Tile using thread-local arrays :
(placed in a local memory stack frame. Allocated in device global memory, but cached in L1)

## Slide 46: Tile using both L1 and read-only cache
__global__ void tiled_local_arrays(…)
{
double ay_local[TILE_FACTOR]; // Thread-local arrays
double by_local[TILE_FACTOR]; // (placed in local memory)
int t = threadIdx.x + blockIdx.x*blockDim.x;
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
{
for( int y = yy; y < yy + TILE_FACTOR; y++ )
{
ay_local[y-yy] = ay[y*N+t];
by_local[y-yy] = by[y*N+t];
}
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay_local[y-yy]
+ bx[x*N+t]*by_local[y-yy];
}
}
X-dependent loads cached in read-only
Thread-local arrays for
Y-dependent loads (cached in L1)
On Kepler, 48 KB read-only cache and 64 KB L1+shared cache are independent. Use both!
Tile using thread-local arrays :
(placed in a local memory stack frame. Allocated in device global memory, but cached in L1)

## Slide 47: Tile using both L1 and read-only cache
On Kepler, 48 KB read-only cache and 64 KB L1+shared cache are independent. Use both!
Tile using thread-local arrays :
(placed in a local memory stack frame. Allocated in device global memory, but cached in L1)
Chart: Tile with L1+Read-Only Runtimes
| Naïve | 2 | 4 | 8
Runtime | 0.138 | 0.093 | 0.347 | 0.293
Chart: l1_cache_local_hit_rate
| TILE_FACTOR 2 | 4 | 8
Runtime | 0.9999 | 0.2313 | 0.007
Fast for TILE_FACTOR = 2! L1 cache fields all y-dependent loads (100% hit rate)
Slower for TILE_FACTOR = 4 and 8. Hit rate decreases.
__global__ void tiled_local_arrays(…)
{
double ay_local[TILE_FACTOR]; // Thread-local arrays
double by_local[TILE_FACTOR]; // (placed in local memory)
int t = threadIdx.x + blockIdx.x*blockDim.x;
for( int yy = 0; yy < NS; yy += TILE_FACTOR )
{
for( int y = yy; y < yy + TILE_FACTOR; y++ )
{
ay_local[y-yy] = ay[y*N+t];
by_local[y-yy] = by[y*N+t];
}
for( int x = 0; x < NS; x++ )
for( int y = yy; y < yy + TILE_FACTOR; y++ )
output[N*(NS*y+x)+t] = ax[x*N+t]*ay_local[y-yy]
+ bx[x*N+t]*by_local[y-yy];
}
}
X-dependent loads cached in read-only
Thread-local arrays for
Y-dependent loads (cached in L1)

## Slide 48: Tile with explicit register use (“unroll-and-jam”)
Kepler SM has 65,536 4B registers = 262 KB of near-core memory available as registers.
>2.5X more than read-only and L1 caches combined.
__global__ void unroll_and_jam_by2_registers(…)
{
// Encourage these to be placed in registers
double ay_local0, by_local0, ay_local1, by_local1;
int t = threadIdx.x + blockIdx.x*blockDim.x;
#pragma unroll 1
for( int yy = 0; yy < NS; yy += 2 )
{ ay_local0 = ay[(yy+0)*N+t];
by_local0 = by[(yy+0)*N+t];
ay_local1 = ay[(yy+1)*N+t];
by_local1 = by[(yy+1)*N+t];
#pragma unroll 1
for( int x = 0; x < NS; x++ )
{
output[N*(NS*(yy+0)+x)+t] = ax[x*N+t]*ay_local0
+ bx[x*N+t]*by_local0;
output[N*(NS*(yy+1)+x)+t] = ax[x*N+t]*ay_local1
+ bx[x*N+t]*by_local1;
}
}
}

## Slide 49: Tile with explicit register use (“unroll-and-jam”)
Kepler SM has 65,536 4B registers = 262 KB of near-core memory available as registers.
>2.5X more than read-only and L1 caches combined.
__global__ void unroll_and_jam_by2_registers(…)
{
// Encourage these to be placed in registers
double ay_local0, by_local0, ay_local1, by_local1;
int t = threadIdx.x + blockIdx.x*blockDim.x;
#pragma unroll 1
for( int yy = 0; yy < NS; yy += 2 )
{ ay_local0 = ay[(yy+0)*N+t];
by_local0 = by[(yy+0)*N+t];
ay_local1 = ay[(yy+1)*N+t];
by_local1 = by[(yy+1)*N+t];
#pragma unroll 1
for( int x = 0; x < NS; x++ )
{
output[N*(NS*(yy+0)+x)+t] = ax[x*N+t]*ay_local0
+ bx[x*N+t]*by_local0;
output[N*(NS*(yy+1)+x)+t] = ax[x*N+t]*ay_local1
+ bx[x*N+t]*by_local1;
}
}
}
Y-dependent loads reused
x times in x-loop

## Slide 50: Tile with explicit register use (“unroll-and-jam”)
Kepler SM has 65,536 4B registers = 262 KB of near-core memory available as registers.
>2.5X more than read-only and L1 caches combined.
__global__ void unroll_and_jam_by2_registers(…)
{
// Encourage these to be placed in registers
double ay_local0, by_local0, ay_local1, by_local1;
int t = threadIdx.x + blockIdx.x*blockDim.x;
#pragma unroll 1
for( int yy = 0; yy < NS; yy += 2 )
{ ay_local0 = ay[(yy+0)*N+t];
by_local0 = by[(yy+0)*N+t];
ay_local1 = ay[(yy+1)*N+t];
by_local1 = by[(yy+1)*N+t];
#pragma unroll 1
for( int x = 0; x < NS; x++ )
{
output[N*(NS*(yy+0)+x)+t] = ax[x*N+t]*ay_local0
+ bx[x*N+t]*by_local0;
output[N*(NS*(yy+1)+x)+t] = ax[x*N+t]*ay_local1
+ bx[x*N+t]*by_local1;
}
}
}
Y-dependent loads reused
x times in x-loop
X-dependent loads used twice

## Slide 51: Tile with explicit register use (“unroll-and-jam”)
In practice I like this approach. Helpful on Kepler, Maxwell, and Pascal.
At 50% occupancy you can use up to 64 registers (32 DP values) for tiling. Unrolling by 2 or 4 is not too annoying for a few performance-limiting kernels.
…but don’t do it for all your kernels.
“Premature optimization is the root of all evil”
Kepler SM has 65,536 4B registers = 262 KB of near-core memory available as registers.
>2.5X more than read-only and L1 caches combined.
__global__ void unroll_and_jam_by2_registers(…)
{
// Encourage these to be placed in registers
double ay_local0, by_local0, ay_local1, by_local1;
int t = threadIdx.x + blockIdx.x*blockDim.x;
#pragma unroll 1
for( int yy = 0; yy < NS; yy += 2 )
{ ay_local0 = ay[(yy+0)*N+t];
by_local0 = by[(yy+0)*N+t];
ay_local1 = ay[(yy+1)*N+t];
by_local1 = by[(yy+1)*N+t];
#pragma unroll 1
for( int x = 0; x < NS; x++ )
{
output[N*(NS*(yy+0)+x)+t] = ax[x*N+t]*ay_local0
+ bx[x*N+t]*by_local0;
output[N*(NS*(yy+1)+x)+t] = ax[x*N+t]*ay_local1
+ bx[x*N+t]*by_local1;
}
}
}
Chart: Unroll and Jam Runtimes
| Naïve | UJ by 2 | UJ by 4 | UJ by 8
Runtime | 0.138 | 0.103 | 0.12 | 0.115
Y-dependent loads reused
x times in x-loop
X-dependent loads used twice

## Slide 52: Cooperative pattern
Each grid point handled by a single thread a warp.
__global__ void warp_team(…)
{
int warpid = ( threadIdx.x + blockIdx.x*blockDim.x )/32;
int laneid = threadIdx.x%32;
int t = warpid;
#pragma unroll 1
for( int y = laneid; y < NS; y += 32 )
{
double ayy = ay[NS*t+y];
double byy = by[NS*t+y];
#pragma unroll 1
for( int x = 0; x < NS; x++ )
output[NS*NS*t+NS*x+y] = ax[NS*t+x]*ayy + bx[NS*t+x]*byy;
}
}

## Slide 53: Cooperative pattern
Each grid point handled by a single thread a warp.
__global__ void warp_team(…)
{
int warpid = ( threadIdx.x + blockIdx.x*blockDim.x )/32;
int laneid = threadIdx.x%32;
int t = warpid;
#pragma unroll 1
for( int y = laneid; y < NS; y += 32 )
{
double ayy = ay[NS*t+y];
double byy = by[NS*t+y];
#pragma unroll 1
for( int x = 0; x < NS; x++ )
output[NS*NS*t+NS*x+y] = ax[NS*t+x]*ayy + bx[NS*t+x]*byy;
}
}
Y-dependent loads are coalesced.

## Slide 54: Cooperative pattern
Each grid point handled by a single thread a warp.
__global__ void warp_team(…)
{
int warpid = ( threadIdx.x + blockIdx.x*blockDim.x )/32;
int laneid = threadIdx.x%32;
int t = warpid;
#pragma unroll 1
for( int y = laneid; y < NS; y += 32 )
{
double ayy = ay[NS*t+y];
double byy = by[NS*t+y];
#pragma unroll 1
for( int x = 0; x < NS; x++ )
output[NS*NS*t+NS*x+y] = ax[NS*t+x]*ayy + bx[NS*t+x]*byy;
}
}
Y-dependent loads are coalesced.
X-loads are uncoalesced…BUT next x-iteration accesses next contiguous location in memory…
AND effective cache per grid point is now 32X higher…perhaps next x-load will hit?
X-dependent loads broadcast a value across the warp. Uncoalesced.

## Slide 55: Cooperative pattern best so far!
Each grid point handled by a single thread a warp.
__global__ void warp_team(…)
{
int warpid = ( threadIdx.x + blockIdx.x*blockDim.x )/32;
int laneid = threadIdx.x%32;
int t = warpid;
#pragma unroll 1
for( int y = laneid; y < NS; y += 32 )
{
double ayy = ay[NS*t+y];
double byy = by[NS*t+y];
#pragma unroll 1
for( int x = 0; x < NS; x++ )
output[NS*NS*t+NS*x+y] = ax[NS*t+x]*ayy + bx[NS*t+x]*byy;
}
}
Y-dependent loads are coalesced.
X-loads are uncoalesced…BUT next x-iteration accesses next contiguous location in memory…
AND effective cache per grid point is now 32X higher…perhaps next x-load will hit?
Nvprof confirms: high hit rates => fast kernel!!
nc_cache_global_hit_rate = 95.39%, tex_cache_hit_rate = 95.39%
Chart: Warp Team Runtime
| Naïve | Warp team
Runtime | 0.138 | 0.052
X-dependent loads broadcast a value across the warp. Uncoalesced.

## Slide 56: Downside to cooperative: need different memory layout.
Kernel with each thread handling a grid point
Cooperative kernel
__global__ void naive(…)
{
int t = threadIdx.x + blockIdx.x*blockDim.x;
#pragma unroll 1
for( int y = 0; y < NS; y++ )
# pragma unroll 1
for( int x = 0; x < NS; x++ )
output[N*(NS*y+x)+t] =
ax[x*N+t]*ay[y*N+t] +
bx[x*N+t]*by[y*N+t];
}
__global__ void warp_team(…)
{
int warpid = (threadIdx.x + blockIdx.x*blockDim.x)/32;
int laneid = threadIdx.x%32;
int t = warpid;
#pragma unroll 1
for( int y = laneid; y < NS; y += 32 )
{
double ayy = ay[NS*t+y];
double byy = by[NS*t+y];
# pragma unroll 1
for( int x = 0; x < NS; x++ )
output[NS*NS*t+NS*x+y] =
ax[NS*t+x]*ayy +
bx[NS*t+x]*byy;
}
}
Each warp handles one grid point.
Fast index must be species index x or y (they are symmetric)
for spatially local accesses by warps. For output, y is chosen to be fastest, so that writes are coalesced.
Corresponds to Kokkos::LayoutRight
Grid point index t is fast index for output, ax, ay, bx, by.
Consecutive threads handle consecutive grid points =>
coalesced access.
Corresponds to Kokkos::LayoutLeft

## Slide 57
Chart: Hall of fame
| Naïve | Tiled, TILE_FACTOR 8 | 12.5% occupancy, TILE_FACTOR 4 | Tiled using L1 and readonly, TILE_FACTOR 2 | Unroll-and-jam by 2 | Warp team
Runtime | 0.138 | 0.196 | 0.127 | 0.093 | 0.103 | 0.052

## Slide 58: Kokkos versions
Naïve kernel
Unroll and jam by 2 kernel
parallel_for( N,
KOKKOS_LAMBDA( const int& t )
{
#pragma unroll 1
for( int y = 0; y < NY; y++ )
#pragma unroll 1
for( int x = 0; x < NX; x++ )
output(t,y,x) = ax(t,x)*ay(t,y) +
bx(t,x)*by(t,y);
} );
parallel_for( N,
KOKKOS_LAMBDA( const int& t )
{
double ay_local0, ay_local1;
double by_local0, by_local1;
#pragma unroll 1
for( int yy = 0; yy < NY; yy += 2 )
{
ay_local0 = ay(t,yy+0); ay_local1 = ay(t,yy+1);
by_local0 = by(t,yy+0); by_local1 = by(t,yy+1);
#pragma unroll 1
for( int x = 0; x < NX; x++ )
{
output(t,yy+0,x) = ax(t,x)*ay_local0
+ bx(t,x)*by_local0;
output(t,yy+1,x) = ax(t,x)*ay_local1
+ bx(t,x)*by_local1;
}
}
} );
On GPU, Views are Kokkos::LayoutLeft
(t is fastest index)
Order of x,y doesn’t matter much on GPU. Writes are coalesced either way.
Noticeable (but minor) effect on performance: y before x makes naïve kernel slightly slower and unroll+jam slightly faster. I’m not sure why…TLB issues?
I choose innermost loop index x as rightmost for later portability to CPU. On CPU, Views become LayoutRight, rightmost index becomes fastest, and innermost loop can then vectorize with stride-1 writes.

## Slide 59: Kokkos versions
int team_size = 8;
int vectorlen = 32;
parallel_for( TeamPolicy<>( N/team_size, team_size, vectorlen ),
KOKKOS_LAMBDA( const TeamPolicy<>::member_type& team_member )
{
int team_rank = team_member.team_rank();
int league_rank = team_member.league_rank();
int t = league_rank*team_member.team_size() + team_rank;
parallel_for( ThreadVectorRange( team_member, NY ),
[&]( const int& y )
{
double ayy = ay(t,y);
double byy = by(t,y);
#pragma unroll 1
for( int x = 0; x < NX; x++ )
output(t,x,y) = ax(t,x)*ayy + bx(t,x)*byy;
} );
} );
Warp team kernel**
Views should now be Kokkos::LayoutRight, even on GPU
(rightmost index fastest)
Consecutive vector indices y map to consecutive threads in the warp, so y must be rightmost here for coalesced writes
becomes blockDim.y
becomes blockDim.x
Ranges from 0 to team_size-1.
For vectorlen = 32,
team_rank = warp id within block.
Global block index
For vectorlen = 32,
t = global warp id.
** See the Kokkos Programming Guide ( https://github.com/kokkos/kokkos/blob/master/doc/Kokkos_PG.pdf ) for details on team policies and hierarchical parallelism.
Hierarchical parallelism

## Slide 60
Chart: Cuda vs. Kokkos runtimes
| Naïve | Unroll-and-jam by 2 | Warp team
Cuda version | 0.138 | 0.103 | 0.052
Kokkos version | 0.17 | 0.118 | 0.047
Kokkos is slower.
Could be reduced occupancy
due to register pressure.
Kokkos version uses 38 registers/thread.
38*256 = 9728 registers/block,
65,536/9728 = 6.74 => only 6 blocks of 256 threads can be live on each Kepler SM.
Theoretical occupancy = 6*256/2048 = 75%.
achieved_occupancy = 0.735
Register pressure?
I don’t know why Kokkos is faster!
I know Kokkos version uses L1 instead of
readonly cache though.
l1_cache_global_hit_rate = 91.65%,
nc_cache_global_hit_rate = 0.00%

## Slide 61: Questions?
michael.carilli.ctr@us.af.mil
mcarilli@gmail.com
https://www.linkedin.com/in/mfcarilli/
https://github.com/mcarilli
(I’ll post runnable example code if/when it gets cleared for public release)